## Slide 1: Concurrent Logic and Interconnect Delay Estimation using MTDDD for behavioral model generation*
Sambuddha Bhattacharya
C-J. Richard Shi
Department of Electrical Engineering
University of Washington, Seattle WA
{sbb,cjshi}.ee.washington.edu
*Supported by NSF-ITR

## Slide 2: Key Objectives
Develop efficient models for delay and noise estimation
Develop efficient Methodology for Verification
Breakthrough Approach: Symbolic Analysis Mixing Boolean and Algebra for Concurrent Gate and Interconnect Delay Estimation

## Slide 3: Motivation
Efficient Verification of circuits
  Millions of transistors and R,L,C parasitic elements
  Spice simulations too slow
  Can live with estimation with less than 10% errors
Insight on interconnect networks and gate inputs
  Delay is a function of
    Input logic pattern
    transistor size
    input slope
    input event,
    parasitic element
    output load
Reducing performance gap between custom and semi-custom

## Slide 4: History of Interconnect Modeling and Reduction
Interconnect modeling
Numerical reduction of interconnect models
  Elmore model estimates signal delay of RC model
    First moment of the impulse response of a network
  AWE
    Considers higher moments
    Moments derived from state equations
    Transfer functions are comprised of moments
  PVL, PRIMA, etc.
Now
Traditionally

## Slide 5: Methods of Logic Delay Estimation
Calculation of Single Equivalent Resistance
Estimating Load seen by the logic block based on moment matching
Numerical methods
Position-based resistance model adds accuracy
Logic and Interconnect together forms a switched R(L)C circuit.
Single delay expression of the whole network under any input
Traditional Methods
Difference from the traditional …

## Slide 6: Symbolic Delay Estimation for Logic blocks
SAMBA: Symbolic Analysis Mixing Boolean and Algebra for Concurrent Gate and Interconnect Delay Estimation
  Incorporates signal delays symbolically
  Combines Boolean sensitizing functions and state equations
  Considers all possible Boolean sensitizing conditions in a logic block
Circuit Equations
Notes: The boolean expressions seen in the matrix prevent singularity’s from occurring. If B is off, the node 2 is forcibly set to 0v.
The addition of the boolean variables allows this single matrix equation to describe the circuit behavior completely under any input sensitization

## Slide 7: Semi-Symbolic Delay Estimation for Interconnects
Semi-Symbolic Moment Calculation, Delay and Noise Analysis with Multi-Terminal Determinant Decision Diagrams
  Semi-symbolically
    Key components kept as symbols
    Less important components represented numerically
  Calculates circuit moments
    Delay and noise in interconnect networks
      Damping factor
      Natural frequency
      Normalized overshoot
      Propagation delay
Many Such Delay Metrics Reported

## Slide 8: Interconnect Tree Driven by an AOI321 Gate
Delay variation of NAND Gate due to variations in CL
Wp varied
AOI321 block followed by large interconnect Network

## Slide 9: Interconnect Tree Driven by an AOI321 Gate
Wn varied
AOI321 block followed by large interconnect Network

## Slide 10: Interconnect Tree Driven by an AOI321 Gate
Load varied
AOI321 block followed by large interconnect Network

## Slide 11: Interconnect Tree Driven by an AOI321 Gate
Resistance varied
AOI321 block followed by large interconnect Network
AOI: Multiple-input
AND-OR-Invert block

## Slide 12: As an Analysis Tool : Comparison of Delay Metrics
Propagation delay in balanced tree with variation in one load capacitor
Propagation delay in unbalanced tree with variation in inductor
NO metric is good for every parameter range

## Slide 13: Schedule
Jan. to Feb. 2003:
  Integrate models with Logic Abstractor
  Extend models to geometry and design parameters
  Test on Boeing’s Digital Pressure Belt (report at Feb. PI meeting)