## Slide 1: CoSMoS: Coupled Simulation and Modeling of Systems-on-Chips
Bo Wan, Bo Hu, Lili Zhou
Advisor: Professor Richard Shi
University of Washington
{wanbo, hubo, llzhou}@ee.washington.edu
Supported by DARPA/NEOCAD
ODT
BMAC:
Behavioral Model Analyzer and Compiler

## Slide 2: What’s Model Compiler?
A Model Compiler is a CAD tool that supports fast prototyping of device models.
Model Compiler
BMAC
Input
Output
Input: compact device models described in high level behavioral language VHDL-AMS*
Output: device code in C/C++ that can be directly compiled in Cosmos/spice.

## Slide 3: Merging into target circuit simulator
C/c++ Device files
COSMOS/spice
Solver source files
Compile & Link
COSMOS simulator
(with an ability to simulate the new Device)
BMAC

## Slide 4: Example: MOSFET Level 1 Model
Input: VHDL-AMS file(s)
(Device Interface definition…)
(Device Interface definition…)
……
MOSequations: procedural is
begin -- procedural statements
IF vds > 0 THEN -- forward
IF vgs <= vthres THEN
-- cut off
ids := 0.0;
ELSE
IF vgs-vthres <= vds THEN -- saturation
ids := Beta * (((vgs - vthres)**2.0) / 2.0);
ELSE -- triode
ids := Beta * ((vgs - vthres)*vds - ((vds**2.0)/2.0));
END IF;
END IF;
ELSE ids := 0.0;
END IF;
end procedural;

## Slide 5: Example: MOSFET Level 1 model
Outputs: a set of C codes files (device calculation codes and the interface to the target circuit simulator-Cosmos simulator)
ask_gen1.gh ask_gen2.gc defs_gen1.gc defs_gen2.gc defs_gen3.gh
  del_gen1.gh dest_gen1.gh dev_gen1.gh dev_gen2.gc dev_gen3.gc
  dev_gen4.gc ext_gen1.gh itf_gen1.gc itf_gen2.gc load_gen1.gh
  load_gen2.gc load_gen3.gc load_gen4.gc load_gen5.gc load_gen6.gc
  load_gen7.gc mask_gen1.gh mask_gen2.gc mdel_gen1.gh mpar_gen1.gh
  mpar_gen2.gc param_gen1.gh param_gen2.gc setup_gen1.gh setup_gen2.gc
  setup_gen3.gc temp_gen1.gh temp_gen2.gc temp_gen3.gc wbr.c wbrask.c
  wbrdefs.h wbrdel.c wbrdest.c wbrext.h wbritf.h wbrload.c wbrmask.c
  wbrmdel.c wbrmpar.c wbrpar.c wbrset.c wbrtemp.c makedefs
The C codes look like:
vgs = gat_across - src_across;
p_vgs_gat_across = 1;
p_vgs_src_across = -1;
vds = drn_across - src_across;
p_vds_drn_across = 1;
p_vds_src_across = -1;
drn_through = +( ids );
p_drn_through_ids = +1;
src_through = -( ids );
p_src_through_ids = -1;
…
…
d_lhs1_drn_across = 0;
d_vgs_src_across = 0 + p_vgs_src_across;
d_vds_src_across = 0 + p_vds_src_across;
d_lhs1_src_across = 0;
d_vgs_gat_across = 0 + p_vgs_gat_across;
d_lhs1_gat_across = 0;
}
…

## Slide 6: Why Model Compiler?
TIME
COST
Designer
Device Model Developer

## Slide 7: Long time & High cost
New device &Equations
Initial coding in MATLAB
Convert to C code
Purchased by design company & Qualification
Release new simulator
Designers using new model
Install & test of the model in simulator
New modification
So Many Bugs!
TOO LONG TIME!!!
New effect update

## Slide 8
Revolution with BMAC:
New device
In VHDL-AMS*
BMAC + Simulator
Direct Communication
Short and quick path
Designer
Model Developer
Better Model. Improved Design.
Save Time. Lower Cost
Fast simulation due to optimized codes

## Slide 9: Abstract Syntax Tree (AST) Representation of Model Equations
AST example for MOS FET Level I model

## Slide 10: BMAC Architecture

## Slide 11: Optimization Methods Used in BMAC
To get the maximum gain of simulation speed up, BMAC uses several methods to optimize the generated device codes:
Constant Node Propagation
Node Reduction
Node Sharing
Bypass
Green Node Optimization

## Slide 12: AST-DRIVEN CODE OPTIMIZATION
Constant Node Propagation :
/
log
*
B3SOIvcrit
*
/
27.0
CONSTCtoK (273.15)
+
Charge_q (1.60219e-19)
Kb (1.3806226e-23)
sqrt
*
2.0
1.0e-14
CONSTvt0
B3SOIvcrit
0.73026894

## Slide 13: AST-DRIVEN CODE OPTIMIZATION
Redundant nodes can be removed!
Node Reduction
Ids
??
??

## Slide 14: AST-DRIVEN CODE OPTIMIZATION
Bypass
  Node Bypass
*
1
v1
V1_new
+/-
0.0
v1
V1_new
*
-1
v1
V1_new

## Slide 15: AST-DRIVEN CODE OPTIMIZATION
Bypass
  2. Device Bypass
Save evaluated values
From previous evaluation
Changed too much?
Check node voltages
Re-evaluation
Yes
No
Continue

## Slide 16: AST-DRIVEN CODE OPTIMIZATION
Node Sharing
*
+
*
+
subtree
Pattern Matching

## Slide 17: AST-DRIVEN CODE OPTIMIZATION
Node Sharing
*
+
subtree
Pattern Matched

## Slide 18: AST-DRIVEN CODE OPTIMIZATION
Green Node Optimization
AST to be evaluated

## Slide 19: AST-DRIVEN CODE OPTIMIZATION
Green Node Optimization
Dyeing Process
AST to be evaluated
Basic Criteria:
The leaf nodes of Green node only contain Constant, model parameter and instance parameter
The leaf nodes of Red node may contain device voltage node

## Slide 20: AST-DRIVEN CODE OPTIMIZATION
Green Node Optimization
Dyeing Process
AST to be evaluated
Cutoff Green Node

## Slide 21: AST-DRIVEN CODE OPTIMIZATION
Green Node Optimization
Dyeing Process
AST to be evaluated
Cutoff Green Node
Code Generation
Gray?
One-time
operations
Yes
Iterative
Operations

## Slide 22: One-time operation VS Iterative operation
CPU time distribution for circuit VCO
Before Green Node Optimization
Iterative device loading
LU Decomposition
Matrix Solving
Other
Onetime Graph and
Output handling
Onetime Device Setup
Onetime circuit parsing

## Slide 23: One-time operation VS Iterative operation
Iterative device loading
LU Decomposition
Matrix Solving
Other
Onetime Graph and
Output handling
Onetime Device Setup
Onetime circuit parsing
CPU time distribution for circuit VCO
After Green Node Optimization
Total CPU time was reduced
from 10.1s to 7.44s
(26.34% saving)

## Slide 24: AST-DRIVEN CODE OPTIMIZATION Summary
Compared to directly generated codes without any global optimization:
Constant Node Propagation: 50% speed up achieved
Node Reduction: 60% speed up achieved
Node Sharing: 50% speed up achieved
Bypass: 40% speed up achieved
Green Node Optimization: 3-4 times speed up achieved

## Slide 25: Experimental Results
Device Models Implemented by BMAC so far
Device Model
# Nodes
# Parameters
Complexity
(#line of VHDL-AMS code)
MOS Level 1
4
2
40
MOS Level 3
4
121
870
BSIM3
4
412
2228
BSIMSOI
6
787
6660
EKV
4
40
116

## Slide 26: Experimental Results
Table 2. Benchmark Circuits
Circuit
# Transistor
One-shot
22
VCO
10
Power AMP
4
Ring Oscillator
12
Comparator
38
INV
2
NAND
4
NOR
4
AOI22
16
OAI22
16
Adder
55
Complex Cell
50
INV chain
8
12-bit Adder
660

## Slide 27: Experimental Results
Scalable
100x-1000x
speed up!!!

## Slide 28: Experimental Results
comparable
Next step goal?

## Slide 29: Experimental Results

## Slide 30: Experimental Results
Boeing Comparator

## Slide 31: Summary of BMAC
BMAC has, for the first time, successfully implemented industry -grade device models including BSIM, BSIM-SOI, EKV using VHDL-AMS and yielded the exactly simulation results as the model code implemented manually.
BMAC is shown to be the first automatic model compiler that is comparable in efficiency to human optimized code (SPICE3).
For a set of test cases, BMAC compiled code with SPICE3 is 100 to 1000 times faster than the best commercial version of the behavioral VHDL-AMS/Verilog-AMS simulators used for compact device model compilation.
“Way ahead of industry” ---- Ken Kundert, Cadence Fellow
“Potentially BIG impact to semiconductor industry” --- Justin Harlow
SRC Director

## Slide 32: Schedule
Dec. 2002: First release of BMAC for device modeling
June 2003: BMAC release with frequency domain support/behavioral modeling
Dec. 2003: BMAC release with nonlinear time solver SILCA
Dec. 2003: BMAC release with digital modeling
June 2004: Final release of BMAC

## Slide 33: Questions?
Thank you!