## Slide 1: CosMos Solver Development
Research Team Members:
  Dr. Guoyong Shi (Lead)
  Zhao Li, Bo Hu, Bo Wan, Lili Zhou
Mixed Signal CAD Research Lab
Electrical Engineering Dept.
University of Washington

## Slide 2: Linear and Nonlinear Solver for CoSMoS
Evaluation of public solvers
Innovative nonlinear/time-domain solver
TECHNICAL OBJECTIVES :
  - Linear Solver: speedup!
  - Solver integration: circuit and EM
  - Optimized nonlinear/time-domain for circuits
  - Accuracy (wide dynamic ranges: derivatives)

## Slide 3: Public Solvers
SuperLU (Direct solver)
Sparse 1.3 (SPICE solver)
AZTEC (Iterative solver)
HYPRE (Iterative solver)
DASSL (DAE solver)

## Slide 4: Feature of SuperLU*
* Developed by Berkeley, Xerox Palo Alto Research Center, NERSC, 1995
Supernode implementation
Cache usage
Column elimination tree for preordering
Symbolic factorization
Real/Complex solve

## Slide 5: Sparse 1.3 vs SuperLU
Compare the performance
Identify weakness for improvement
Sparse 1.3
- A circuit-specific direct solver (1985)
SuperLU
- A general purpose direct solver (1995)

## Slide 6: Sparse 1.3 vs SuperLU
Design and Implementation
Sparse 1.3
Initial order/factor
(Markowitz) - reusable
Numerical factorization
(G.E.)
Solve (standard)
SuperLU
Preorder by elim tree
- reusable
Numerical factorization
(Supernode based G.E.)
Solve (standard+refine)

## Slide 7: Testing Sparse & SuperLU
Matrix data
- Source: Many Circuits, FE/FD, Artificial.
- Type: Dense, sparse, real, complex
- Size: 1k – 100k
Internal matrix format
- Sparse: Linked list
- SuperLU: Column compressed format

## Slide 8: Comparison
Numerical factorization and solving
- No great difference (on average).
Ordering and symbolic factorization
- Notable difference for most cases:
Markowitz-based preordering might not
  be efficient as implemented in Sparse.
Sparse vs SuperLU

## Slide 9: Numerical Factor Time

## Slide 10: Solve Time

## Slide 11: Benchmark Circuit
Matrix | Size | Order+ Factor | 2nd Factor | Solve | Order | Factor | Solve
M1 | 100k | 7.6 | 0.05 | 0.04 | 0.23 | 0.36 | 0.09
M2 | 200k | 31.6 | 0.11 | 0.10 | 0.58 | 0.78 | 0.17
M3 | 300k | 71.3 | 0.17 | 0.15 | 0.84 | 1.13 | 0.26
M4 | 500k | 198.6 | 0.27 | 0.26 | 1.36 | 1.92 | 0.42
M5 | 800k | 512.1 | 0.45 | 0.39 | 2.31 | 3.18 | 0.75
Sparse 1.3
SuperLU
Ladder circuits, matrices are tridiagonal.
Time in sec.

## Slide 12: Benchmark circuit
Matrix
Order+Factor (sec)
SearchPivot (sec)
Elimimation (sec)
M1
7.65
7.33
0.05
M2
31.60
31.03
0.07
M3
71.31
70.32
0.21
M4
198.66
197.21
0.28
M5
512.11
509.24
0.39
Time split of Order+Factor (Sparse 1.3)

## Slide 13: Sparse - searching pivot
Sparse 1.3 – Not efficient in searching a pivot.
Tridiagonal matrix
– quadratic growth !
matrix size
sec

## Slide 14: SuperLU - Preordering
Technique: Column Elimination Tree
  Performs better in most cases, but not
  perfect.
  - Could be incorporated in Sparse solver.
* Column ordering is a key issue in the speed of direct solvers.

## Slide 15: Iterative Solvers
AZTEC (Iterative solver)
HYPRE (Iterative solver)
Potential solvers for EM and coupled EM/CKT.
(To be integrated and tested.)

## Slide 16: DAE Solver - DASSL
DASSL – A FORTRAN package developed by
    Prof. Linda R. Petzold
    (1983, widely used).
(To be integrated and tested.)

## Slide 17: Integration of Solvers
Direct solvers
Iterative solvers
DAE solvers
EM solvers

## Slide 18: EM solvers and CKT solvers
System matrix with CKT and EM components:
EM solver – Iterative, precondition, sparse/dense.
CKT solver – Direct (LU), more efficient.
Need an integrated solver to solve the whole system efficiently !

## Slide 19: Conclusion
Possible to speedup Sparse 1.3.
Some techniques in SuperLU are powerful.
DAE solvers and iterative solvers are other
  options.
Integration with EM solvers is necessary.
Need a prototype design for integration.

## Slide 20: Schedule on Linear Solver
CoSMoS
Next Quarter (Jan – Mar, 2003):
  Speedup Sparse 1.3 (pivoting efficiency).
  Incorporate some features of SuperLU in Sparse.
  (Finish 1st version of direct solver.)
Next 6 months (-- June 2003):
  Integration of Iterative solvers, DAE solvers, and EM solvers.
  (1st version of integrated CKT/EM solver.)
Next year (-- Dec 2003):
  Test, debug, enhanced versions.

## Slide 21: SILCA Semi-Implicit Linear Centric Analysis
PhD Student: Zhao Li
Advisor: Prof. Richard Shi
Mixed Signal CAD Research Lab
Department of Electrical Engineering
University of Washington, Seattle WA
lz2000@ee.washington.edu
CoSMoS Time-Domain Nonlinear Solver

## Slide 22: Time-Domain Simulation
Time-domain simulation is essential for the final verification of System-On-Chip (SOC) designs. Numerical integration is typically implemented in two ways:
  Variable-time-step methods are applied to achieve a balance between # of actual simulation points and accuracy (LU factorization and MNA matrix load are needed for each simulation point)
  Fixed-time-step methods are applied to reduce the LU factorization and MNA matrix load cost (A relatively small time step is required to ensure accuracy)

## Slide 23: Time-Domain Simulation – Our Objectives
Keep using variable-time-step methods
Introduce a new semi-implicit integration formula to exploit the benefit of fixed-time-step methods
Apply an iterative linear solver to ensure simulation stability and achieve more relaxation

## Slide 24: Semi-Implicit Trapezoid Formula
Trapezoid formula
New formula for variable-time-step integration (  is the variable-time-step factor)
LU once!

## Slide 25: Direct Semi-Implicit Solver
To ensure simulation stability,  must be less than 1 in theory
To satisfy the LTE requirement,  should be close to 1
In practice, we found  can only be varied between 0.9 and 1.05, the relaxed SPICE can achieve this too

## Slide 26: Iterative Semi-Implicit Solver
The Semi-Implicit solution is used as an initial guess for an iterative solver to find a final Implicit solution  Stability and accuracy are ensured!
In practice, we found  can be varied more widely (between 0.667 and 2)  more relaxation is achieved

## Slide 27: Linear Circuit Analysis Example
A stiff circuit example  two RCL circuits with 100X time constant difference
Initial time step 0.01 sec, simulation interval 160 sec, 16001 simulation points are needed for fixed-time-step methods

## Slide 28: Comparison of CoSMoS Linear Time-Domain Solvers with SPICE
Although more iterations are introduced for linear circuit solving, its overhead may be decreased when combined with nonlinear circuit solvers
354
11518
1974
CoSMoS Iterative Semi-Implicit
1266
4892
1950
CoSMoS Direct Semi-Implicit
1678
5254
1962
Relaxed SPICE
2635
5260
1967
SPICE
#LU
#Iterations
#Simulation
points
Method

## Slide 29: Nonlinear Simulation
In SPICE-like simulators Newton-Raphson (NR) iteration is implemented. But its drawbacks are well-known:
  Nonlinear functions must be continuous and (at least) first-order differentiable
  LU factorization is needed at each iteration
  Nonlinear function derivatives evaluation and related MNA matrix load are required at each iteration (solved by CoSMoS BMAC!!!)
  Its quadratic convergence rate is ruined due to practical considerations

## Slide 30: Nonlinear Simulation Alternative
Successive Chord (SC), or piece-wise weakly nonlinear, method to speed up the nonlinear simulation – LU once!
Piecewise linear (PWL) method is used to find DC operating points
Our goal – DC operation point guess is found with the PWL method. The rest analysis is achieved by the variable SC method

## Slide 31: Variable Successive Chord Method
Different chords are used for different regions
Achieve a balance between convergence speed and LU factorization cost
Rank-1 update to reduce LU

## Slide 32: Comparison of Four CoSMoS Nonlinear Solvers with SPICE
+ Including the iterative semi-implicit linear solver
* Dependent on practical applications, typically the
same as #Iterations
5936
289032
31511
CoSMoS SC+
5617
275613
32184
CoSMoS Variable SC+
46419
145824
31756
CoSMoS Variable SC
45494
178444
31002
CoSMoS SC
*
135561
30960
SPICE
#LU
#Iterations
#Simulation points
Method

## Slide 33: Conclusion on Linear and Nonlinear Time-Domain Solvers
SILCA – A prototype of Time-domain Nonlinear Circuit Simulator
Variable-time-step numerical integration
Iterative Semi-Implicit solver
PWL method (to be improved and tested)
Variable SC method (to be improved and tested)
*** Orders of magnitude faster
*** Work without derivatives if needed

## Slide 34: Schedule on NonLinear Solver
Next Quarter (Jan  Mar, 2003)
  Rank-one update for the variable SC method
  Integration of Table-look-up MOSFET models
Next 6 months ( June 2003)
  Integration of nonlinear capacitors
  Integration of PWL solver
  Optimize the solver implementation
  (Finish 1st version of nonlinear solver)
Next year ( Dec 2003)
  Integration with VHDL-AMS simulator