## Slide 1: PARASITIC-AWARE DESIGN AND OPTIMIZATION FOR CMOS ULTRA-WIDEBAND AMPLIFIERS
Jinho Park and Prof. David Allstot
Electrical Engineering / University of Washington
Supported by DARPA/NEOCAD

## Slide 2: History
1996: Birth of “Parasitic-Aware” Design and Optimization (Dr. David Allstot)
1998: Parasitic-aware design and optimization of CMOS RF ICs by Dr. Ravi Gupta and Dr. Allstot (RFIC symposium / MTT-s / JSSCC)
1999: CMOS distributed amplifier design using CAD optimization techniques by Ballweber and Dr. Allstot (ISSCC / JSSCC)
2000: A 0.5-8.5GHz fully-differential CMOS RF distributed amplifier by Dr. Ahn and Dr. Allstot (SSMSD / JSSCC)
2002: Parasitic-aware synthesis of RF CMOS switching power amplifiers by Kiyong and Dr. Allstot (ISCAS)
2002: Parasitic-aware design and optimization of CMOS wideband amplifiers by Jinho Park and Dr. Allstot (ASP-DAC)
2003: Parasitic-aware optimization of CMOS RF circuits by Jinho Park, Kiyong, and Dr. Allstot (Kluwer Academic Publishers)

## Slide 3: Can we use CMOS for RF?
Factors | GaAs | Si-CMOS
Ft | 90GHz | 75GHz1 (0.13μm)
Noise | Very low | Bad1
Breakdown voltage | High | Low1
Substrate | Semi-insulating | Highly doped2
Qs of passives | 20~50 | 5~122
Integration | 50K | >100M devices
Cost | $2.50 per cm2 | $0.25 per cm2
Si-CMOS performance limited by active1 and passive2 devices
Very low cost / high integration = system-on-chip
Next: active improvement

## Slide 4: CMOS DA Example[1]
[1] B. Kleveland, et al., “Monolithic CMOS distributed amplifier and oscillator”, ISSCC99.

## Slide 5: CMOS DA Example[2]
[2] B.M. Ballweber, R. Gupta, and D.J. Allstot, “A fully integrated 0.5-5.5GHz CMOS distributed amplifier,” ISSCC99.
Parasitic-laden Inductor

## Slide 6: CMOS DA Example[2]
Simulation
Measured

## Slide 7: Motivation
Advantages of CMOS
  Low cost / High integration / Scaling
Disadvantages
  Poor performance due to parasitics
  Solved by parasitic-aware design based on SA
Problems in 1DA using parasitic-aware based on 2SA
  Low gain of distributed amplifier
  CMOS High Gain wideband Matrix Amplifier
  Long optimization time (a day with 9 design variables on HP712/100)
  A New Parasitic-Aware Optimization Technique based on fast Particle Swarm

## Slide 8: Matrix Amplifier
Problems of DA
  Additive gain (need many section)
  Large area
  Loss associated with delay line (Metal resistance + gate / drain resistance)
    Optimum number of sections 4~5 (<10dB S21)
Additive + Multiplicative by stacking more than one delay lines (2-D)
Gain is K times bigger in dB than DA with smaller area
  Sharing delay lines
Next: DA/MA summary

## Slide 9: Schematic (2X4 Matrix)
Spec: S21 ~20dB BW >12GHz in 0.25μm CMOS
Used maximum # of sections: 4
  Maximize BW and minimize ripple
Cascode
  Minimize capacitive coupling between delay lines (gain flatness)
  Improve reverse isolation
  Compensate for loss by increasing Rds
M-derived half section
  Buffering between delay lines and termination resistors (gain flatness)
shared
delay line
Next: phase linearity

## Slide 10: Structure of Parasitic-Aware Synthesis and Optimization
Optimization Core
(particle swarm)
Circuit Simulator
(HSpice / Spectre)
Parasitic Modeling
Request
Parasitic
Generate
Netlist
Parasitic
Value
Simulation
Results
Next: inductor model
CoSMOS

## Slide 11: Parasitic Inductor Modeling
What do we need? – S-parameter data for each inductor
(1) Measurement data – Min, Mid, Max
  Used for calibration of EM simulator
(2) EM simulator – calibration and interpolation
(3) SPICE inductor model (freq. and inductance)
  Curve fitting (polyfit)
    e.g. Rs = a3*f3 + a2*f2 + a1*f + a0
    a3 = b5*L5+b4*L4+b3*L3+b2*L2+b*L+b0
Next: circuit simulator

## Slide 12: Particle Swarm
Inspired by a social behavior of a swarm of bees searching for the location of food
Exchange individual and group information to find the optimum (Cooperation)
Work on a population of potential solution candidates called Particles
  Inherently parallel process (use of population)
Well-balanced between global / local search
  Very fast
Very Simple and Easy to be implemented as optimization core for parasitic-aware synthesis and optimization

## Slide 13: Swarming Equations
Motion of searching agents (Particles) by keeping track of individual and group experience (Competition and Cooperation)
  inertia competition
  cooperation
Next: bees

## Slide 14: Initialization
Random 1)position
2)velocity

## Slide 15
Update of Position & Velocity
Vector sum
inertia
tendency
toward the best

## Slide 16: SA Particle Swarm
Origin
  Physical process of annealing
History
  Old, well studied
Agent?
  Single
Initial point dependent?
  Yes
Implementation?
  easy
Speed?
  Known to be Slow
Chance to trap in local?
  probable in complex tasks
Parallelization?
  Possible
Origin
  Social behavior of bees
History
  New, need to be studied
Agent?
  Population
Initial point dependent?
  No
Implementation?
  easy
Speed?
  Known to be Fast
Chance to trap in local?
  Low
Parallelization?
  Inherently parallel process
Next: Apply to MA and DA

## Slide 17: Which technique is better?
Two different parasitic-aware synthesis
    Simulated Annealing – Conventional optimization core
    Particle Swarm – New optimization core
Will Particle Swarm fit parasitic-aware synthesis?
DA (11 variables)
MA (16 variables)
Next: design target

## Slide 18: Comparison Results
Comparable initial performance for both DA and MA
Performance difference increases as the constraints become tighter and the total iterations increase.
SA performs very poor in complex tasks.
  Particle swarm is 1) faster and more 2) efficient.
Next: MA results
Acceptable Solution line

## Slide 19: Optimization Results (MA)
Next: how to optimize
Gain
Phase shift

## Slide 20: How to optimize?
Problems
  Reduced gain (S21)
    Gain is not added up in phase due to addition of parasitic capacitance (no valid phase synchronization)
    Resistance attenuates the signal propagation
  Reduced bandwidth
    Added capacitance / resistance
  Manual design is impossible because of non-linear behavior between parasitics
Solving using optimization
  Regain phase synchronization by finding proper values of inductance, capacitance
Next: Final design

## Slide 21: Final Design Results Summary
Factors | Before optimization | After optimization
Average Gain (S21) | 15.2 | 19.5
Gain flatness (S21) | ±2.5 | ±0.6
Std. deviation (S21) | 1.13 | 0.36
Max. S11 in passband | -14.4 | -12
Max. S12 in passband | -77 | -67.3
Max. S22 in passband | -6.6 | -7.2
Cutoff frequency (GHz) | 10.5 | 12.5
Unity-gain freq. (GHz) | 11.5 | 14.5

## Slide 22: Conclusions
CMOS matrix amplifier achieved very high gain with wide bandwidth.
  ~20dB, flat gain over 12GHz
New parasitic-aware synthesis and optimization with particle swarm used
  Very fast / efficient
  Parallel process