## Slide 1: DDD-based Symbolic Circuit Analysis
Ph.D. Candidate: Alicia Manthe
Ph.D. Student: Zhao Li
Advisor: C.-J. Richard Shi

## Slide 2: Overview
Symbolic Circuit Analysis
  Simulators
  Analog Design Flow
  Characteristics
  Applications
Determinant Decision Diagrams
Symbolic Approximation
DDD Optimization
Nonlinearity Analysis
Future Research
Conclusion

## Slide 3: Simulators
Numerical Simulators: SPICE, Spectre
Symbolic Simulators: SCAPP, ISSAC
Numerical
Simulator
Symbolic
Simulator

## Slide 4: Analog Design Flow
Analog Design Process
Analog Design Process with
Symbolic Circuit Analysis
Symbolic Circuit Analysis Fits In!

## Slide 5: Symbolic Circuit Analysis
Symbolically Characterizes:
  Gain
  Impedance
  CMRR
  Pole-Zero
  Noise Figures
  Distortion/Harmonics
  Intercept points (IP3)

## Slide 6: Symbolic Circuit Analysis
Applications:
  Gain Design Insight
  Design Space Exploration
  Sensitivity Analysis
  Behavioral Model Generation
  Fault Detection
  Noise Analysis
  Distortion Analysis

## Slide 7: Overview
Symbolic Circuit Analysis
Determinant Decision Diagrams
  Cramer’s Rule
  DDD Vertex Expansion
  DDD Creation
Symbolic Approximation
DDD Optimization
Nonlinearity Analysis
Future Research
Conclusion

## Slide 8: Cramer’s Rule
Exponential Growth!!
system equation:

## Slide 9: DDD Vertex Expansion
1-edge 0-edge
Sign
Vertex
label = A
*Shi & Tan, TCAD 2000
*
+
Cofactor
Remainder

## Slide 10: Determinant Decision Diagram
MNA
Create
DDD
Derive
H(s)

## Slide 11: DDD Complexity
Create
DDD
0
5
10
15
20
25
30
10
0
10
1
10
2
10
3
10
4
10
5
10
6
10
7
10
8
matrix dimension -- n
#Product-Terms (#Product-Terms) x n #DDD-Vertices
 Generally orders of magnitude smaller
 Ladder Circuits: Linear time complexity O(n)
Vertex Order:
AGDFCBE

## Slide 12: Overview
Symbolic Circuit Analysis
Determinant Decision Diagrams
Symbolic Approximation
  Review
  Results
DDD Optimization
Nonlinearity Analysis
Future Research
Conclusion

## Slide 13: Symbolic Approximation
Complex DDD-based Techniques
  Node Contraction
  Device Elimination
S-Expanded DDD-based Algorithms
  Coefficient Suppression
  Symbolic Cancellation
  Device Elimination on Coefficients
  Generation of Dominant Terms

## Slide 14: Node Contraction
If Np & Dp are dominant then f is simplified to:
Node Contraction - Factorization

## Slide 15: Example: Node Contraction
Circuit structure reduction – N0 is contracted and all devices connected to it are eliminated

## Slide 16: Device Elimination
If & are dominant then f is simplified to:

## Slide 17: Example: Device Elimination
Circuit structure reduction – Branches between N1 & N2 are eliminated

## Slide 18: Symbolic Approximation
Complex DDD-based Techniques
  Node Contraction
  Device Elimination
S-Expanded DDD-based Algorithms
  Coefficient Suppression
  Symbolic Cancellation
  Device Elimination on Coefficients
  Generation of Dominant Terms

## Slide 19
S-Expanded DDD

## Slide 20
Coefficient Suppression
Contribution of xisi in numerator and denominator are different and frequency dependent
Typically, higher-order powers of s can be ignored

## Slide 21
Symbolic Cancellation
Generating dominant terms without Cancellation
  Greatly degrades output response
Do cancellation on different patterns
  Based on
    MNA formulation
    Device matching
  Example
    a*b*c cancels –a*d*f if b==d & c==f

## Slide 22
Symbolic Cancellation: 2 patterns
Lemma
  For each product term containing L1 & L4, there exists a corresponding canceling product term containing L2 & L3

## Slide 23
Device Elimination on Coefficients
Observation
  For a specific coefficient, it’s commonly dominated by a small number of devices
  Device elimination can be done coefficient by coefficient
    Notice that it can’t be related to circuit reduction since different devices will be eliminated for different coefficients

## Slide 24
Generation of Dominant Terms
Observation
  Many small-signal characteristics dominated by a small number of product terms
    a*b + c*d dominated by a*b
      if magnitude of a, b, c, d are 1e3, 1e0, 1e0, 1e-1
Solution
  Extraction of k most significant product terms can be transformed to the problem of finding k shortest path weighted in DDD
  User specifies accuracy

## Slide 25: New Breakthrough 1: Extraction of k significant terms
Tan’02
Linear time algorithm O(kn) (exponential, previously!!)

## Slide 26
 | #Terms in Num | Power of s in Num | #Terms in Den | Power of s in Den | MaxErr in Mag | MaxErr in Phase
Exact | 8.98e+16 | 0~22 | 6.39e+19 | 0~22 | 0% | 0%
Fact | 4.69e+08 | 0~13 | 2.20e+11 | 0~13 | 5.96% | 6.30%
Dev Elim | 30176 | 0~7 | 382200 | 0~8 | 15.83% | 10.17%
Suppress | 24568 | 0~4 | 172698 | 0~4 | 20.61% | 10.17%
Decan | 2120 | 0~4 | 11518 | 0~4 | 20.61% | 10.17%
Coeff Elim | 530 | 0~4 | 1754 | 0~4 | 20.61% | 10.17%
Generat of Dominant | 10 | 0~2 | 47 | 0~4 | 17.88% | 15.93%
a741 Example

## Slide 27
a741 Example

## Slide 28
a741 Example

## Slide 29: Overview
Symbolic Circuit Analysis
Determinant Decision Diagrams
Symbolic Approximation
DDD Optimization
  Review
  Results
Nonlinearity Analysis
Future Research
Conclusion

## Slide 30: DDD Vertex Order Dependence
Vertex Order:
A C D F G H B E I J
Vertex Order:
A C D F B G H E I J
How do we choose this order?

## Slide 31: DDD Optimization
Order of vertices influences size of DDD
  Linear to exponential in size
Reduces evaluation time & space complexities
  Proportional to size of DDD
Reduces manipulation time & space complexities
  Proportional to size of DDD
Synthesis: reduces complexity of hardware
  Proportional to hardware costs

## Slide 32: Algorithms for BDD Optimization
Exact
  w/lower bounds
Sifting
  w/lower bounds
Windowing
Symmetry
Scatter Search
Dynamic Variable Reordering

## Slide 33: DVR Example
Reduced by 3!!!

## Slide 34: DDD Lower Bounds
Examining the possible DVR scenario’s:
  Lemma 1: Each label must be represented at least once in the DDD, therefore
    1  #vertices’(xi)
  Lemma 2: Local exchanges between label order i and i+1
    ½#vertices(xi)  #vertices’(xi)  2#vertices(xi)
    ½#vertices(xi+1)#vertices’(xi+1)2#vertices(xi+1)
#nodes with label xi+1 in DDD before reorder
#nodes with label xi+1 in DDD after reorder

## Slide 35: Lower Bounds
Sifting down a label (i → i+1)

## Slide 36: Sifting w/lower bounds Results
Ran several different types of circuits:
  Amplifiers, RLC circuits, Filters
% decrease in #nodes is highly dependent on original order chosen

## Slide 37: Exact Results
circuit | N | #Vertices |  |  | #Swaps |  | 
 |  | before | after |   | No Prune | With Prune |  
E1 | 2 | 2 | 2 | 0 | 2 | 2 | 0
E4 | 3 | 3 | 3 | 0 | 18 | 30 | 167
2x2 | 4 | 4 | 4 | 0 | 144 | 264 | 183
E5 | 5 | 6 | 5 | 17 | 1201 | 1161 | 97
E8 | 6 | 6 | 6 | 0 | 10800 | 19500 | 181
Opamp | 6 | 8 | 6 | 25 | 12139 | 5308 | 44
RC | 7 | 9 | 7 | 22 | 105848 | 31843 | 30
E9 | 7 | 9 | 7 | 22 | 105841 | 31671 | 30
E10 | 7 | 8 | 7 | 13 | 105849 | 32657 | 31
E11 | 8 | 12 | 8 | 33 | 1128967 | 48068 | 4
E16 | 9 | 12 | 9 | 25 | 13063696 | 95752 | 1
E13 | 9 | 12 | 9 | 25 | 13063686 | 168111 | 1
3x3 | 9 | 13 | 12 | 8 | 13063682 | 527118 | 4
Fig.1 | 10 | 13 | 10 | 23 | X | 347270 | X
TwoStage | 10 | 16 | 10 | 38 | X | 545452 | X
E15 | 11 | 15 | 12 | 20 | X | 14430117 | X
E14 | 12 | 22 | 13 | 41 | X | 5889044 | X
Ran several different types of circuits:
  Amplifiers, RLC circuits
  Random matrices with differing symbol locations, number of symbols, and size of matrix
Due to the number of permutations kept in memory some cases were unable to finish, represented by X

## Slide 38: DDD Optimization Conclusions
Using the DDD LB method can significantly reduce the number of vertices
Using lower bounds during sifting can dramatically decrease computation cost by an average of 50%
Using DDD lower bounds vs. BDD lower bounds can decrease computation time up to 8%
Exact DDD minimization reduced DDDs between 10-40% for some already reduced DDDs
Lower/Upper bounds requires less than 5% computation than without
Notes: <number>
<footer>
<header>
<date/time>

## Slide 39: Symbolic Circuit Analysis Optimization
Create
DDD
MNA
Optimize
DDD
Run
Analysis
Symbolic
Approx.
X
X
50-90%
reduction
10%-30%
reduction

## Slide 40: Overview
Symbolic Circuit Analysis
Determinant Decision Diagrams
Symbolic Approximation
DDD Optimization
Nonlinearity Analysis
  Review
  Preliminary Results
Future Research
Conclusion

## Slide 41: Analog Design Criteria
Performance criteria
  Transfer function accuracy
  Power consumption
  Linearity
    Limits value of largest useful signal
  Noise performance
    Limits value of smallest useful signal
Useful
Dynamic
Range

## Slide 42: Third-Order Intermodulation Distortion Ratio
Measures third-order distortion component
  Dominants in fully differential circuits
Nonlinear
System
Johns & Martin, Analog Integrated Circuit Design, John Wiley & Sons, New York, 1997.

## Slide 43: Third-Order Intercept-point
The Higher the Intercept point the more the 3rd-order harmonics are suppressed
For every 1dB A is decreased ID3 improves by 2dB
Input level A
Output level A
→ an is represented by a transfer function and in terms of a DDD

## Slide 44: Nonlinearities
Strongly
  Digital logic controlling the operations of analog/RF front-ends
    Leads to abrupt behavior changes
  Behavioral models for system-on-chip simulation characterized by PWL models
Weakly
  Small excursions around the quiescent point

## Slide 45: Weakly Nonlinear Analysis
Numerical Algorithms
  Harmonic Balance
  Shooting Methods
  Describing Functions
Symbolic Algorithms
  Volterra
    Can obtain closed-formed explicit expressions to represent harmonic and intermodulation distortion terms

## Slide 46: Volterra Series Approach
Nonlinear element has controlling current i1
Nodes can be regarded as sum of harmonics and intermodulation products:
  Vx,m,n: phasor of component of voltage at node x at frequency mw1+nw2
Nonlinear
network
iin1
iin2
F. Fernandez, A. Rodriguez-Vazquez, J. Huertas, G. Gielen. Symbolic Analysis Techniques. New Jersey: IEEE Press, 1998.

## Slide 47: Linearize Network
Add nonlinear current source to linearize nonlinear elements in circuit
  Determines higher order distortion terms
  Expression based on previous calculation of node voltages
q
p
gm(Vi,1,+/-1, Vj,1,+/-1)
i
j
iNL2gm

## Slide 48: Symbolic Strongly Piecewise Linear Circuit Analysis
Model strongly nonlinear behavior
    Switching operating regions
    Sudden changes of device physics
Model any piecewise linear function
    I-V characteristics

## Slide 49: PWL Concepts
“New” Orthoator
  u  0
  j  0
  uj = 0.
Used to model
PWL behavior
Polarity opposite of an ideal diode

## Slide 50: Modeling PWL function
Leenaerts & Bokhoven, Piecewise Linear Modeling and Analysis, Kluwer Academic Publishers, 1998.

## Slide 51: MNA Stamping Rule
Compact macro circuit

## Slide 52: MNA Formulation
What about j and u?
Mixed Linear Complementarity Problem!?!

## Slide 53: Explicit Solution to Linear Complementarity Problem
An orthoator
  q > 0 then j = -q/d, u = 0
  q  0 then j = 0, u = q
  j = -q/d and u = q
    where:
2-Dimensional
j
-u+

## Slide 54: Complementarity Decision Diagram
Need an efficient diagram to represent the explicit solution to LCP
  1-D
  2-D
Sharing
@(n-2)

## Slide 55: Symbolic PWL Analysis on Strongly Nonlinear Circuits
Create
DDD
CDD
Create
LCP
Run
Analysis
MNA*

## Slide 56: a741 Behavioral Model

## Slide 57: PWL Conclusions
Modeled circuits with hard nonlinearities using PWL functions
Implemented
  DDD-based procedure for converting MLCP to LCP
  Efficient graph-based form of LCP
Tested on several different circuits
  a741, mixer, etc.

## Slide 58: Conclusions
Reviewed
  Symbolic Circuit Analysis
  Symbolic Approximation
  Optimization Techniques
  Nonlinearity Analysis

## Slide 59: Preliminary Schedule
Research | Schedule
Characterize solution to LCP in freq. domain | Winter – Spring 2003
Approx. corners of PWL for volterra partial derivatives | Winter – Spring 2003
Fully implement PWL/Volterra interfaces | Spring – Summer 2003
Test on a various analog designs | Spring – Summer 2003
DDD-based approx. of symbolic expressions | Summer 2002
Mixed symbolic/numeric analysis | Summer 2003
Efficient symbolic pole/zero generation | Summer 2003

## Slide 60: Thank you!
Questions?