## Slide 1: Device Modeling with Behavioral Language VHDL-AMS*
Students: Lili Zhou (PhD Candidate)
Kishore Tanikella (PhD Candidate)
Christopher Baker (Undergraduate RA)
Gus Mak (Undergraduate RA)
Advisors: Prof. Richard Shi
Dr. Pavel Nikitin
Time: 12/09/2002
Mixed Signal CAD Lab, University of Washington
D
A
R
P
A

## Slide 2: Outline
Introduction to behavioral language modeling
  Importance
  Brief introduction on VHDL-AMS
Current work—modeling BSIM3 /B3SOI/EKV MOS model
  Overview of BSIM3 and B3SOI models
  Model Implementation in VHDL-AMS/ Verilog-AMS
Test examples
  BSIM3 model
  B3SOI model
Mixed Signal CAD Lab
D
A
R
P
A

## Slide 3
feedback
New device &Equations
Initial coding in MATLAB
10-30K Lines!!!
Convert to C code
Purchased by design company & Qualification
Release new simulator
Designers using new model
Install & test of the model in simulator
New modification
So Many Bugs!
TOO LONG TIME!!!
Device modeling today

## Slide 4: Modeling with VHDL-AMS and automatic model compiler
New device
In VHDL-AMS*
BMAC + Simulator
Direct Communication
Short and quick path
Designer
Model Developer
Better Model. Improved Design!!!
Save Time.Lower Cost!!!

## Slide 5
VHDL-AMS
VHDL-AMS(IEEE Std. 1076.1-1999+ IEEE Std. 1076-1993)
  Extension to VHDL (IEEE Std. 1076-1993, VHSIC Hardware Description Language) supports the description and simulation of event-driven systems.) to support the description and simulation of analog and mixed-signal circuits and systems.
Adds new simulation models supporting continuous behavior
  Continuous models based on differential algebraic equations (DAEs)
  DAEs solved by dedicated simulation kernel: the analog solver
  Handling of initial conditions, piecewise-defined behavior, and discontinuities
  Optimization of the set of DAEs being solved and how the analog solver computes its solution are outside the scope of VHDL-AMS
Mixed Signal CAD Lab
D
A
R
P
A

## Slide 6
VHDL-AMS
Extended structural semantics
  Conservative semantics to model physical systems
    e.g. Kirchhoff’s laws for electrical circuits
  Non-conservative semantics for abstract models
    Signal-flow descriptions
  Mixed-signal interfaces
    Models can have digital and analog ports
Mixed-signal semantics
  Unified model of time for a consistent synchronization of mixed event-driven/continuous behavior
  Mixed-signal initialization and simulation cycle
  Mixed-signal descriptions of behavior
Frequency domain support
  Small-signal frequency and noise modeling and simulation
Mixed Signal CAD Lab
D
A
R
P
A

## Slide 7: Current Work
Implementation of device models in behavioral languages (VHDL-AMS and Verilog-AMS)
  BSIM3 MOS model
  B3SOI MOS model
  EKV model( Presented by Christopher Baker and Gus Mak)
Implement behavioral circuit model
Validation of BMAC
Mixed Signal CAD Lab
D
A
R
P
A

## Slide 8: BSIM3 MOS model
BSIM3 is a physics-based, accurate, scalable, robust and predictive MOSFET SPICE model for circuit simulation and CMOS technology development.
It is developed by the BSIM Research Group in the Department of Electrical Engineering and Computer Sciences (EECS) at the University of California, Berkeley.
The third iteration of BSIM3 (commonly abbreviated as BSIM3v3), was established by SEMATECH as the first industry-wide standard of its kind in December of 1996. BSIM3v3 has since been widely used by most semiconductor and IC design companies world-wide for device modeling and CMOS IC design.
Mixed Signal CAD Lab
D
A
R
P
A

## Slide 9: BSIM3 MOS model
The development of BSIM3v3 is based on Poisson's equation using gradual channel approximation and coherent quasi 2D analysis, taking into account the effects of device geometry and process parameters. BSIM3v3.2.2 considers the following physical phenomena observed in MOSFET devices.
  Short and narrow channel effects on threshold voltage.
  Non-uniform doping effect (in both lateral and vertical directions).
  Mobility reduction due to vertical field.
  Bulk charge effect.
  Velocity saturation.
  Drain-induced barrier lowering (DIBL).
  Channel length modulation (CLM).
  Substrate current induced body effect (SCBE).
  Subthreshold conduction.
  Source/drain parasitic resistances.
Mixed Signal CAD Lab
D
A
R
P
A

## Slide 10: BSIM3 MOS model
Mixed Signal CAD Lab
library IEEE;
  package electrical_system is
  nature electrical is real across real through;
terminal ground : electrical;
end electrical_system;
entity wbr is
generic(
-- Default value Processing for BSIM3 MOSFET Models
n : integer := NMOS;
………………
mBSIM3nfactor : real := 1.0;
mBSIM3xj : real := 0.15e-6;
……………..
);
port ( terminal drain, gate, source, bulk : electrical);
end entity wbr;
architecture BSIM3V3 of wbr is
quantity vdsq across drain to source;
quantity vgsq across gate to source;
…………………
begin MOSequations: procedural is
………. ………
variable mBSIM3vcrit, mBSIM3factor1, mBSIM3vtm : real ;
Idq := n*hBSIM3mode*Ids + n*qdrn'dot - n*hBSIM3cbd;
Ibq := n*qbulk'dot + n*Isub + n*hBSIM3cbs;
………. ………..
end procedural;
end architecture BSIM3V3;
D
A
R
P
A

## Slide 11: B3SOI MOS model
Mixed Signal CAD Lab
BSIMSOI is a deep submicron, Silicon-on-Insulator MOSFET device model for SPICE engines. It is developed by the BSIMSOI Group in the Department of Electrical Engineering and Computer Sciences at the University of California, Berkeley.
BSIMSOI was selected by EIA Compact Model Council as the industry standard SOI MOSFET model in December 2001.
D
A
R
P
A

## Slide 12: B3SOI MOS model
Mixed Signal CAD Lab
D
A
R
P
A

## Slide 13: B3SOI MOS model
Mixed Signal CAD Lab
D
A
R
P
A

## Slide 14
Implement models in VHDL-AMS/ Verilog-AMS
Mixed Signal CAD Lab
entity soiwbr is
generic(
mB3SOItype : integer := NMOS;
mB3SOImobMod : integer := 1;
mB3SOIcapMod : integer := 2;
……………..
);
port ( terminal drain, gate, source, ebulk : electrical);
end entity soiwbr;
architecture B3SOI of soiwbr is
quantity vdsq across drain to source;
quantity vesq across ebulk to source;
quantity vpsq across pbody to source;
quantity Idq through drain;
quantity Ibq through body;
quantity Ieq through ebulk;
…………………
begin MOSequations: procedural is
begin
hB3SOIcd := Ids + Ic - Ibd + Iii + Idgidl;
………………
Ibq := mB3SOItype*(Ibs + Ibp + Ibd - Iii - Idgidl-Isgidl-Igb);
Idq := mB3SOItype*(Ids + Ic - Ibd + Iii + Idgidl) +Vvds*1.0e-9+ mB3SOItype*qdrn'dot;
……………..
end procedural;
end architecture B3SOI;
D
A
R
P
A

## Slide 15
Test Examples(BSIM3): Boeing’s design-- Comparator
Mixed Signal CAD Lab
D
A
R
P
A

## Slide 16
Test Examples(BSIM3): VCO
Mixed Signal CAD Lab
D
A
R
P
A

## Slide 17
Test Examples(BSIM3): One-Shot Pulse Generator
Mixed Signal CAD Lab
D
A
R
P
A

## Slide 18
Test Examples(BSIM3): Power Amplifier
Mixed Signal CAD Lab
D
A
R
P
A

## Slide 19
Test Examples(BSIM3): Ring Oscillator
Mixed Signal CAD Lab
D
A
R
P
A

## Slide 20
Test Examples(B3SOI): I-V curve
Mixed Signal CAD Lab
D
A
R
P
A

## Slide 21
Test Examples(B3SOI): Inverter
Mixed Signal CAD Lab
D
A
R
P
A

## Slide 22: Preliminary Implementation of EKV Model v2.6
Background
Process
  Equations
  Code (Verilog)
    Simulation, Graphs
    Debug
  Verilog >> VHDL

## Slide 23: EKV Background
Simulation Model
  Low voltage
  Low current
  Analog, Digital mixed signal
Uses fundamental physical properties
http://legwww.epfl.ch/ekv/

## Slide 24: Equations
EKV v2.62 equations
  Geometrical and process
  Doping effects
  Substrate
  Weak, moderate, strong inversion layer
  Mobility effects
  Thermal effects
One set of equations continuous over all regions

## Slide 25: Sample Behavioral Implementation
  // 6.1: Dynamic model for the intrinsic node charges
  nq = 1 + (Gamma_a/(2 * pow((Vp + phi + 1e-06),0.5)));
  xf = pow((0.25 + i_forward),0.5);
  xr = pow((0.25 + i_reverse),0.5);
  qD = -nq*((4/15)*((3*xr*xr*xr+6*xf*(xr*xr)+4*xr*(xf*xf)+2*(xf*xf*xf))/pow((xf+xr),2))-0.5);
  qS = -nq*((4/15)*((3*xf*xf*xf+6*xr*(xf*xf)+4*xf*(xr*xr)+2*(xr*xr*xr))/pow((xr+xf),2))-0.5);
  qI = qS + qD;
  qox = 0;
  if( Vg_prime > 0 )
  begin
  qB = -Gamma_a * (pow((Vp + phi + 1e-06),0.5))*(1/Vtherm)-((nq-1)/nq)*qI;
  end
  else
  begin
  qB = -Vg_prime * 1/Vtherm;
  end
  // Total charge
  qG = -qI-qox-qB;

## Slide 26: Simulation and Debug
Resistor/Inverter circuit
  NMOS
Debug
Figures

## Slide 27: Figure 1.1 DC Response

## Slide 28: Figure 1.2 Transient Response

## Slide 29: Plan for Next Step
Debug Verilog
Add PMOS
Test with bigger circuits
Verilog >> VHDL

## Slide 30
Mixed Signal CAD Lab
Thank you!
Q&A