## Slide 1: Electromagnetic Modeling of Integrated Circuit Systems
Pavel Nikitin, Richard C.-J. Shi
December 10, 2002

## Slide 2: Outline
Introduction
EM effects in IC systems
Numerical EM methods
Circuit-EM interaction
Unified language
Future work

## Slide 3: Introduction
Density, functionality, and speed of integrated circuits increase each year
EM effects start affecting system performance when wavelength becomes comparable to system dimension
Accurate EM simulation of the coupled system is necessary in many cases – for SoC, SiP, PCB

## Slide 4: Challenges
Many EM solving tools are available, each with specific capabilities and limitations
Proper use of them for IC design is non-trivial, especially if designer is not an EM expert
Unlike circuit problems, there is no industry standard for describing and treating EM problems
EM structure behavior depends on its environment

## Slide 5: Electromagnetic Effects
On-chip EM structures behavior
  RF components, transmission lines
Parasitics and coupling
  Substrate
  Package
  Interconnects
  Power-ground network
Radiation and interference (EMI)

## Slide 6: EM Solving Methods
Differential equation methods
  Finite difference (FD, FDTD, TLM)
  Finite element method (FEM)
Integral equation methods
  Method of moments (MoM)
  Boundary element method (BEM)
Hybrid methods

## Slide 7: Method Comparison
Method | Unknowns | Resulting matrix | Solution domain | Capability
Differential | Fields in volume | Sparse | Time (FDTD), frequency (FEM) | Complex geometry and materials
Integral | Currents on conducting parts | Dense | Frequency | Limited

## Slide 8: Defining Circuit-EM Interaction
Equivalent representation of EM structures
  EM structures are modeled separately from circuits as equivalent circuits or S-parameter blocks
Direct field-circuit interaction
  Time-stepping EM solution (FDTD) and circuit solution are interlaced in time
Coupled formulation
  Circuit and EM equations are coupled together in a single MNA matrix (PEEC), the interaction is defined via voltages and currents at common ports

## Slide 9: Unified Language
A unified hierarchical language
  Is capable of describing a complex mixed system at various abstraction levels
  Provides a communication interface between parts of the system that have different nature
Example: VHDL-AMS
  Describes mixed digital and analog circuit systems
  Allows one to include MEMS devices, thermal effects

## Slide 10: VHDL-AMS(E)
Proposition
  VHDL-AMS can be extended to include capability for EM modeling, new extended language can be called VHDL-AMS(E)
Advantages
  Solver-independent system description
  EM-circuit communication interface
  Hierarchical modeling of EM systems
  Facilitation of model exchange between designers

## Slide 11: EM Modeling Vision

## Slide 12: Conclusions
A unified language description of mixed EM-circuit systems is an attractive approach
Study of EM modeling requirements from the language perspective is necessary
Defining EM-circuit interaction and study of hierarchy in EM systems are open research topics

## Slide 13: Milestones
Language requirements
  April 2003
Hierarchy in description of EM systems
  June 2003
EM-circuit interaction mechanisms
  September 2003
Interfacing with existing EM solvers
  December 2003

## Slide 14: Useful References
A. Ruehli, A. Cangellaris, “Progress in the methodologies for the electrical modeling of interconnects and electronic packages”, Proceedings of the IEEE, vol. 89, no. 5, May 2001
R. Achar, M. Nakhla, “Simulation of high-speed interconnects”, Proceedings of the IEEE, vol. 89, no. 5, May 2001
W. Kao, C. Lo, M. Basel, R. Singh, “Parasitic Extraction: Current State of the Art and Future Trends”, Proceedings of the IEEE, vol. 89, no. 5, May 2001
B. Romanowicz, “Methodology for the modeling and simulation of microsystems”, Kluwer Academic Publishers, 1998